## Slide 1
ADVANCED THIN FILM
RESEARCH LABORATORY
(2008)
Dr. PhD&Ing. R. M. Oksuzoglu
Faculty of Engineering / Department of Material Science and Engineering
AU-TFG

## Slide 2
Facilities / Capabilities
Custom-Design UHV Multi-Chamber Sputtering Deposition Tool
Metal Chamber (6 Sources)
Metal-Oxide Chamber (4 Sources and Ion/Atom-Source)
Self-constructed software (up to 100 sequences)
Annealing Chamber (700 C)
Load Lock (up to 12 samples)
Deposition and Process Techniques
Transfer between chambers
DC&RF-Magnetron
Pulsed DC-Magnetron
Reactive Deposition
DC-Assisted RF-Magnetron
Ion/Atom Insertion
In-Situ-Magnetic Field
In-Situ DC-Bias
Uni-directional Magnetic Field
Annealing
AU-TFG

## Slide 3
Facilities / Capabilities
Structural, Electrical and Magnetic Characterization
X-Ray Diffractometer (up to 4 inch wafers)
Scanning Probe Microscopy (SPM, AFM, LFM)
Surface Profiler (up to 4 inch wafers)
Four Point Probe station with heating stage
Helmholtz Coil (Magnetoresistance)
New Tools (Pending): Combination of
Vibration Sample Magnetometer- AND
Micro-Probe Electrical Transport-Systems
AU-TFG

## Slide 4: Sputtering and Deposition Parameters
Base Pressure of Deposition Chamber (Torr)
Deposition Pressure (mTorr)
Deposition Flow (Ar-sccm)
Deposition Power (Watt)
Partial Pressures (Ar-O2-N2)
Working Distance (h)
Working Angle (Φ, θ)
Depositon rate (nm/s)
Uniformity (h, r, l )
Rotation Speed of Substrate (rpm)
Substrate Temperature (°C)
Techniques depending on the Materials:
Metallic: DC-Sputtering
Semiconductor: DC or RF Sputtering
Insulator: RF-Sputtering
AU-TFG

## Slide 5
Research Areas /1
THIN FILM STRUCTURES AND SYSTEMS (NANO-MAGNETISM)
Spin Valves
  Ta/Ru/Ta/NiFe/Pt-IrMn/CoFe/Ru(/CoFeB/New-Barrier (0.8 – 1.5nm)/ CoFeB/Ta/Ru/Au
  Ta/Ru/Ta/IrMn/CoFeB/New-Barrier (0.8 – 1.5nm)/CoFeB/Ta/Ru/Au
Exchange Bias
  Seed-Layer/IrMn/Interface-Modification/CoFe/Ta
  New Seed-Layer/IrMn/CoFe/Ta
SUBJECTS
Magnetoresistance Random Access Memory (MRAM), Read Heads and Position sensors
  Giant&Tunnel Magnetoresistance (GMR&TMR)
  Resistance-Area Product (RA)
  Thermal Stability

## Slide 6: Sputter Deposition Conditions and Parameters for Simple Spin Valve Sensors
Base Pressure (Torr)
Deposition Pressure (mTorr)
Deposition Flow (Ar-sccm)
Deposition Power (Watt)
Partial Pressures (Ar-O2-N2)
Working Distance (h)
Working Angle (Φ)
Depositiın rate (nm/s)
Uniformity (h, r)
Rotation Speed of Substrate (rpm)
Substrate Temperature (°C)
Deposition Technique
Cap Layer
FreeLayer (FM)
Cu, Mg or Al-Oxide
Pinning Layer
AFM Layer
Under Layers
For each layer
6 – 9 Parameters
For a Simple Spin Valve
42 – 63 Parameters
DC
DC-Pulsed
Reactive
RF
DC
DC-Pulsed
RF
DC
DC-Pulsed
RF
AU-TFG

## Slide 7
sıkıştırılmış tabaka
ayırıcı tabaka
serbest tabaka
bit
GMR | TMR
- Cu (CIP) , CuOx (CPP) | - AlOx veya MgO (CPP)
- Spin dependent scattering | Polarization Difference between electrodes
- ≈ % 15 MR [1] | - ≈ % 600 MR [2]
MR (%) = (ρAP – ρP) / ρP | 
Spin Valve Systems (GMR&TMR) for
Terabyte Memories in Smart-Electronics
[1] S. Jo, M. A. Seigler, J. Magn. Magn. Mater., 316, 93-97 (2007)
[2] Ikeda et al., Appl. Phys. Lett., 93, 082508 (2008)
* http://www.research.ibm.com/research/gmr.html
Ta /Ru/Ta (35nm)
NiFe (8nm)
IrMn/CoFe/Ru (13nm)
CoFeB (2nm)
CoFeB (2nm)
Ta/Au (15nm)
AU-TFG
Substrate
Cap Layer
Free Layer
Barrier Layer
Pinned Layer
Pinning Layer
Seed Layer
Buffer Layer

## Slide 8
Research Highlights /1
Small-Angle X-Ray Diffraction
Ta/NiFe
IrMn
CoFe
Ta
Ta/NiFeCr/Ru
PtMn
CoFe
Ta
X-Ray Reflectivity-Simulations
Exchange Bias in Spin Valve Systems
Magnetic Hysteresis – Theoretical Fitting

## Slide 9
Research Areas /2
THIN FILM STRUCTURES AND SYSTEMS (OPTIC)
Metal Oxide Semiconductors
  Si/SiO2/TiMgOx
  Si/SiO2/VOx/V
  Quartz/VOx
SUBJECTS
Microbolometers (ASELSAN-MGEO, Turkey)
Optical Switch
Non-linear Optic (Cooperation with University – Ankara, Turkey)

## Slide 10
Cap Layer
Free Layer
Barrier Layer
Pinned Layer
Pinning Layer
Seed Layer
Buffer Layer
10
Substrate
Spin Valve and VOx Structures
AU-TFG
Ta /Ru/Ta (35nm)
NiFe (8nm)
IrMn/CoFe/Ru (13nm)
CoFeB (2nm)
CoFeB (2nm)
Ta/Au (15nm)
Total Thickness
~ 100 nm
VOx
VOx < 100 nm is desired for CMOS

## Slide 11
Uncooled Microbalometers: Infrared detectors
Bridge structure of Honeywell microbolometer
Dai, X. Z. Wang, S. W. He et al., “Low temperature fabrication of VOx thin films for uncooled IR detectors by direct current reactive magnetron sputtering method,” Infrared Physics & Technology, vol. 51, no. 4, pp. 287-291, March 2008.
R.A. Wood, C.J. Han, P.W. Kruse, Integrated uncooled IR detector imaging arrays, Proceedings of IEEE SolidState Sensor andActuator Workshop, 132–135, Hilton HeadIsland , S.C., (June, 1992).
In micromachining fabrication of CMOS thin films
The reproducible phase and composition and morphology at low process temperature (<400 ºC)
Film thickness uniformity
Optimization of TCR & resistivity products

## Slide 12
Research Highlights /2
Atomic Force Microscopy
Temperature Coefficient Resistivity
VOx(50nm)
(a) 4 ns and (b) 65 ps pulse durations excitations at several intensities

## Slide 13
Collaborations
Financial Supports
Institute of Material Sciences, Technical University Darmstadt, Germany
Physics of Nanostructures, Technical University Bielefeld, Germany
University Ankara – Non-Linear Optic Research Lab., Turkey
Institute of Materials Science and Nanotechnology (UNAM), Turkey
Gebze Institute of Technology, Nanomagnetism Lab. Turkey
Different Groups within Anadolu University
The Scientific and Technological Research Council of Turkey (TUBITAK)
Prime Ministry State Planning Organization (DPT)
Anadolu University Research Fund (AU-BAP)
ASELSAN-MGEO

## Slide 14
People and Contact Info
Dr. PhD. & Ing. Ramis Mustafa OKSUZOGLU
rmoksuzoglu@anadolu.edu.tr
http://home.anadolu.edu.tr/~rmoksuzoglu
Ph.D Candidates
Mustafa Yıldırım
MSc Students
Murat Yağcı
Sami Pekdemir
Elif Gül Özkan
Okan Deniz (graduated)
Pınar Bilgiç (graduated)
Ogeday Çapar (graduated)
Hakan Çınar (graduated)
Phone: +90 222 321 3550 ext. 6345 and 6382
Fax: +90 222 323 95 01

## Slide 15
Thank you for your attention!